1.	The purpose of the NE Code is:

a) to serve as a design specification.

b) to serve as an instruction manual for untrained people.

c) to provide efficient, safe electrical systems.

d) to provide efficient, convenient, adequate electrical systems.

e) the practical safeguarding of persons and property from hazards arising from the use of

electricity

2.	Some electrical equipment has working parts that might be exposed to the weather. What type enclosure must I use to prevent problems?  (Snow, ice, dust or temperature extremes are not a problem, in this case.)

a)  watertight   	b)  weatherproof	c)  raintight	d) rainproof	e) any of the above

3.	The grounded conductor is the:

a) neutral	b) high-leg	c) "B" phase	d) conductor that is intentionally grounded

4.	A thermal protector, when properly applied, protects a motor against  dangerous over-heating due to:

I) failure to start	II) overload

a) I only	b) II only	c) both I and II		d) neither I or II

5.	What is the minimum lighting required by the NEC around service equipment and some

other electrical areas?

a) 15 foot candles   b)60 foot candles  c) lighting is not required  d) no minimum required

6.	A multi-family dwelling is a building that contains   ______ dwelling units?

a) 2 or more     b) at least 2      c) at least 3                 d) 3 or more

7.	Switchboards, panelboards, industrial control panels and other motor control  centers in other than dwelling occupancies, that are likely to require examination, adjustment, service or  maintenance 	while energized, shall be field marked to warn Qualified Persons of:

a) potential electric arc flash hazards		b) possible danger of electrical shock

c) potential danger of electrical burns		d) unauthorized personnel must not touch

8.	Working space in front of equipment must be at least  ____ inches wide.

a) 24" wide	b) 30" wide	c) 36" wide	d) 40" wide

9.    	Electric equipment shall be installed:

a) in a neat and workmanlike manner.	b) securely, to match other equipment.

c) only by Electrical Contractors.		d) only by Journeyman Electricians.

10.    	A duplex-receptacle outlet is installed to serve a wet sink in a residential dining room.  The outlet 	must be:

a) GFCI protected	b) on small appliance Ckt.	c) on 20-amp Ckt.	d) a,b and c.

11.	The incandescent lampholder to be used when connecting to a 25 amp circuit must have a:

a)  medium base	b) admedium base	c) mogul base	          d) heavy duty base

12.	A single receptacle, on an individual 20-amp branch circuit shall be rated at:

a)  15 A	b)  20 A	c)  15 or 20 A		d)  16 A

13.	Receptacles connected to a 30-amp branch circuit supplying two or more outlets shall be rated

not less than:

a) 40  A	b)  20 A	c)  25 A	d)  30 A

14.	Receptacles in a dwelling unit dining area are required:

a)  to be on a 15-amp circuit.

b)  to be on a separate 20-amp circuit.

c)  for each wall counter space 12-inches or wider.

d)  to be on the 20-amp kitchen appliance circuit.

15.	When used on 20 amp circuits, receptacles shall be rated not less than ____ amps and not more 	than  _____ amps.

a) 15 – 15	b) 15 – 20	c) 20 – 20	d) 15 – 30

16.	How many duplex outlets are required to be installed to serve a kitchen island that is 6 feet long 	and 20 inches wide?

a) at least one		b) at least two		c) at least three	d) at least four

17. 	How many outside, 120-volt outlets, does the NEC require installed on a single--family dwelling?

a) one on each outside wall		b) one on the front wall or back wall

c) one on either outside wall		d) one on the front wall and one on the back wall

18.  	Heating, A/C, and refrigeration equipment requires a 125 volt, 15 or 20 Amp outlet within

______ feet of the equipment location.

a)  25		b) 50		c) 75		d) 100

19.	In dwelling occupancies, the maximum voltage, between conductors that feed screw shell lampholders shall not exceed ______ volts.

a) 150		b) 240		c) 277		d) 120

20.	When the neutral of two branch circuits which are derived from two different systems enter the same enclosure, one neutral may be white (or gray), and the other neutral:

a) gray		b) white	c) white with a colored stripe, not green

21.	In general, live parts of electrical equipment shall be guarded when operating at, or over:

a) 24 volts	b) 50 volts	c) 100 volts	d) 120 volts

22.	Ground fault protection for equipment is required on a 480 volts grounded wye service if the service disconnecting means is rated ________ or more.

a) 500 amps	b) 800 amps	c) 1000 amps	d) 1200 amps

23.	Audible and visual signal devices shall be employed, where practicable, to give warning of 	_____________ of emergency power.

a) malfunction		b) power-outage

c) overvoltage		d) derangement

24.	A storage battery supplying emergency lighting and power shall maintain not less than 87.5 		percent of full voltage at total load for a period of at least:

a) 2-hours		b) 1 1/2 hours	c) 1 hour	d) 1/4 hour

25.	Optical fiber cables are used to transmit____ for control, signaling, and communications through 	an optical fiber.

a) light		b) electrons	c) amp		d) volts

26.	A storage building is near a residence.  A feeder is run in PVC to the storage building from the 		house, and fused at the house service panel.  How is the building required to be grounded?

a)  You can drive a ground rod or ground plate.

b)  You can run an equipment ground from the house.

c)  Either a) or b) would meet NE Code.

d)  Neither a) or b) are correct.

27.	Fixed electric space heating loads shall be calculated at ______% of the connected load.

a)  74%	b)  100%	c)  125%	d)  135%

28.	For a feeder or service supplying household electric ranges, wall mounted ovens, counter--		mounted cooking units and electric clothes dryers, the maximum unbalanced load shall be 	considered as _____ percent of the load on the ungrounded wires.

a)  70		b)  80		c)  90		d)  100

29.	When running circuits on the outside of a building, which of the following  are allowed?

a) multiconductor cable	b)  rigid metal conduit

c) knob-and-tube		d)  any of the above are allowed

30.	The max. rating of a single cord-and-plug connected load used on a 20 A branch circuit shall be:

a) 16 A	b) 10 A	c) 20 A	d) 12 A

31.	The Code states that any available wall space in a residence, measured along the floor line, must 	be within ____ feet of a plug receptacle.

a)  4		b)  6		c)  8		d)10